## Slide 1: PID methods other than RICH
Antonello Di Mauro
(CERN)
RICH2018 Workshop, Moscow – 01/08/2018

## Slide 2
The ALICE example

## Slide 3: The ALICE detector
ALICE is the LHC experiment devoted to the study of QGP in Pb-Pb collisions →
PID essential for a comprehensive investigation
B=0.5 T

## Slide 4: PID techniques in ALICE
Barrel detectors | 
Specific ionization energy loss | ITS (SSD, SDD), TPC
Transition radiation | TRD
Time of flight | TOF (T0)
Single arm | 
Calorimetry | PHOS, EMCAL, DCAL
RICH | HMPID
Muon spectrometry | Muon arm
Pre-shower | PMD

## Slide 5: The ALICE Time Projection Chamber
500 cm
E
E
400 V / cm
beam
field cage
readout chambers
92us
High Voltage electrode
(100 kV)
845 < r < 2466 mm
90 m3 drift gas volume
  Ne/CO2 (90/10) in RUN1
  Ar/CO2 (90/10) in RUN2
e- drift time ~ 100 ms
MWPC R/O with IBF gating grid (10-5)
R/O rate ~ 1 kHz in pp and 200 Hz in Pb-Pb
~560000 R/O pads of 4x7.5, 10,15 mm2
gas filtering and purity monitoring
gain equalization by 83Kr gas runs
laser system for drift velocity calibration and distortion corrections
pp
Pb-Pb

## Slide 6: The ALICE TPC performance
Excellent tracking and PID in high multiplicity environment
Space point resolution σx ≈ 0.3 mm, σy ≈ 0.4 mm
Truncated mean algorithm 60% (max 159 clusters/track)
σdE/dx ≈ 5.2 % in pp
σdE/dx ≈ 6.5 % in central Pb-Pb
Track-by-track PID @ p <1 GeV/c
Statistical unfolding techniques @ p > 1GeV/c

## Slide 7: PID by decay topology
kink: secondary vertex in TPC
Hypernuclei ID
Vertex: ITS and TPC tracking, ct ~ 8 cm
3He and p- ID by dE/dx in TPC
D0 ID
Vertex: ITS and TPC tracking, ct ~ 123 mm
K- (+) and p+ (-) ID by dE/dx in TPC
arXiv:1709.00288v1 [nucl-ex] 1 Sep 2017
Phys. Lett. B 754 (2016) 360

## Slide 8: The ALICE TOF detector
3.7 - 4.0 m
|h| < 0.9, full 𝜑 —> 18 SuperModules(SM)
5 Modules each SM, 15-19 MRPCs (120x7.4 cm2) per module, 2.5x3.5 cm2 R/O pads
total of 141 m2, 152928 R/O channels
93% C2H2F2 + 7% SF6

## Slide 9: The ALICE TOF performance
Eur. Phys. J. Plus (2013) 128
s2TOF= s2MRPC + s2TDC + s2FEE + s2Cal
constant terms
New calibration procedure to correct time slewing at single channel level (see R. Preghenella’s talk)
56 ps

## Slide 10: The ALICE TOF performance

## Slide 11: The ALICE TRD detector
|h| < 0.84, 2π in azimuth → 18 SuperModules
5 stacks in beam direction, 6 layers in radial direction, 522 chambers (18 missing in front of PHOS)
Each chamber consists of a radiator sandwich (RohacellHF71 and polypropylene fibre mats) and a MWPC filled with Xe/CO2 (85:15)
Total active area: ~673 m2
Gas volume: ~27 m3
1.15 million R/O channels
2.9 – 3.7 m
Nucl. Inst. and Meth. A 881 (2018) 88–127
17 mm fibres

## Slide 12: The ALICE TRD detector performance
Excellent agreement with parametrization of dE/dx and TR from various particles and sources (cosmics, testbeam, pp @ 7 TeV), TR onset @ bg > 800
Nucl. Inst. and Meth. A 881 (2018) 88–127
p rejection ~ 410
Different analysis methods:
Truncated mean
Single or multidimensional likelihood (based on signal t evolution)
Neural network

## Slide 13: The ALICE TRD e-trigger performance
Enhancement of 700 wrt minimum bias (TPC+ TOF only)

## Slide 14: Combined PID in ALICE: Bayesian approach
Eur. Phys. J. Plus (2016) 131: 168
Using accurate detector response parametrization → for each particle species (p, K, p, …) conditional probability corresponding to measured detectors signals
Comparison with Monte Carlo and verification by benchmark analysis of known decay channels (V0)
PID from threshold or max probability

## Slide 15: The ALICE Upgrade in LS2 (2019-2020)
The strategy
New ultra-light silicon trackers based on MAPS: ITS (mid-rapidity), MFT (forward rapidity)
New TPC read-out chambers (GEMs) and electronics
New Fast Interaction Trigger (FIT)
New R/O of other detectors (TOF, TRD, PHOS, Muon arm, ZDC, …)
New merged Online and Offline systems (O2 project)
High precision measurements to explore new frontiers in QGP properties
Main requirements
Untriggered data sample
→ fully exploit the 50 kHz Pb-Pb interaction rate delivered by LHC
Improved tracking performance down to very low pT
LoI, March 2013
RUN3+RUN4: 1011 events ~ 13 nb-1 in Pb-Pb ( 100x RUN2 statistics)
Probe rare physics channels
Heavy flavour down to very low pT
Charmonium states
Low mass di-leptons
Light (anti-)nuclei and hyper-nuclei

## Slide 16: ALICE TPC Upgrade
Quadruple GEM stack: combination of Standard (140 mm) and Large Pitch (280 mm) GEM foils
New FEE based on ASIC SAMPA
R/O segmentation and # of channels ~ present TPC
(not to scale)
OROC GEM stack
arXiv:1805.03234v2 [physics.ins-det] 17 Jun 2018
IROC pad plane
Courtesy of C. Lippmann
conservative operation range
extended operation range
Requirements for GEM readout system:
50 kHz Pb–Pb interaction rate, average event spacing: ~20 μs → average pileup: 5 events
Minimize IBF w/o GG and implement continuous R/O
IBF < 1 %
Energy resolution: σE/E < 12% for 55Fe
Preserve spatial and p resolution

## Slide 17
A look beyond the horizon

## Slide 18: A challenging future
https://doi.org/10.1016/j.nima.2018.03.021
With next generation of colliders probability of merged vertices > 10% →
Timing is the key aspect of R&D for future detectors

## Slide 19: 4D tracking
Huge effort from HEP community to reduce pileup adding timing information to tracking
Dissect the luminous region to recover the LHC purity of reconstructed primary vertices (PU ~ 40)
→ ~ 10s ps time resolution
L. Gray, Connecting the Dots - Intelligent Trackers 2017
Beam-spot time spread

## Slide 20: 4D Ultra Fast Silicon Detectors
Low Gain Avalanche Diode
High precision timing requires high S/N and fast rise-time
Best S/N @ ~ 20-30
Additional doping layer (B or Ga)
F. Carnesecchi, 14th Pisa Meeting on advanced detectors 2018
Rep. Prog. Phys. 81, 026101 (2018)
Best thickness ~ 50 mm
Required radiation hardness ~ 2x1015 neq/cm2 achieved by C implant to mitigate B deactivation in gain layer
s2t= s2Landau + s2time slewing + s2jitter + s2TDC

## Slide 21: CMS Endcap Timing Layer
M. Costa, 14th Pisa Meeting on advanced detectors 2018
Sensor state of the art
LGAD produced by FBK, CNM, HPK
1/16 of full module in production
Fill factor under optimization
Double disk structure, aluminium wedge with embedded cooling pipes © @ -30 oC, 42 mm total tickness
2624 sensors of 48 x 96 mm2 , each with 1536 pads of 1x3 mm2
12 m2, 4M channels
Radiation: 2×1015 neq/cm2
(MIP Timing Detector, Phase2 upgrade)
Present situation: fill factor 91% → 96% for 30 mm gap (technological limit)
“trench” design: Fill factor ~ 100%
INFN+FBK RSD project (Resistive AC coupled Silicon Detector): no segmentation of active area, fill factor 100%
Barrel Timing Layer (BTL)
LYSO crystals + SiPM Readout
Endcap Timing Layer (ETL)
LGAD
Hermetic MIP timing layer
between tracker and HCAL

## Slide 22: CMS Barrel Timing Layer
C. Tully, Academic Training Lectures, CERN 12/05/17
A. Benaglia, Talk at ICHEP 2018
(MIP Timing Detector, Phase2 upgrade)
Barrel Timing Layer (BTL)
LYSO crystals + SiPM Readout
Endcap Timing Layer (ETL)
LGAD
Hermetic MIP timing layer
between tracker and ECAL
~10mm x 10mm area LYSO crystals at R=1200mm  Hit occupancy few % at 200 PU
36 trays in ϕ, 72 half trays, 56 modules per half tray, 64 crystals per module
Half-Tray size: 2604 mm x 184.5 mm
40 m2, 258048 channels
radiation: 2×1014 neq/cm2
Operated at -30° C
SiPM active area limited to < 16 mm2 (noise and power dissipation)
ASIC: TOFHiR (adapted from commercially-available TOFPET) : leading edge discrimination + amplitude measurement for time-walk corrections
Target timing resolution demonstrated at beam tests with Hamamatsu and FBK SiPM
However, observed timing dependence on hit position on the tile
Hardware solutions being considered:
  tailored SiPM with uniform tile surface coverage (response is uniform by construction, but large Si area)
  replace crystal tiles with bars read out on both sides

## Slide 23: The ATLAS High-Granularity Timing Detector
Pseudorapidity coverage: 2.4<|η|<4.0
Radial extension: 12 cm < R < 64 cm
z position: 3.5 m
Thickness in z: 7.5cm
2 double planar layers per endcap
LGAD, 50 mm thick, gain 20 (FBK, CNM)
Low occupancy , Pixel size: 1.3x1.3 mm2
radiation: 4.5×1015 neq/cm2
LGAD hit time resolution worsens with radial distance due to larger radiation dose: maintain 30ps/track resolution by increasing the number of hits at low radius → larger overlap of modules at low R
ATL-LARG-PROC-2018-003

## Slide 24: The LHCb TORCH detector
TOF detector considered for LHCb Upgrade II
PID in 2-10 GeV/c momentum range
Exploit prompt production of Cherenkov light to determine TOF
Single photon st ~ 70 ps, track st ~ 15 ps
R&D next goals
single photon resolution of ~100ps (including time reference)
improve calibration/ alignment (e.g. charge-to-width calibration of NINO).
MCP by PHOTEK Ltd, 11/module
53x53 mm2 active area, 64x8 pads
ALD coating for lifetime > 5 C/cm2
NINO +HPTDC R/O electronics
N. Harnew, 14th Pisa Meeting on advanced detectors 2018

## Slide 25: The PANDA TOF detector
AntiProton Annihilation at Darmstadt (FAIR)
•Fixed target (cluster-jet or pellet)
•Collision rate ~ 20 MHz
•Free ﬂowing DAQ with continuous R/O
S. Zimmerman, 14th Pisa Meeting on advanced detectors 2018
16 layers PCB of 2460 x 180 x 20 mm3
used as mechanical support and to transmit the signals to FEE
Measured crosstalk and attenuation
Tested various scintillators (EJ-232, EJ-228)
SiPMT (ASD-NUV3S-P by AdvanSiD) connected in series by 4 for lower effective capacitance and faster signal
s ~ 51 ps
Requirements:
  < 100 ps time resolution
  Event timing + PID below DIRC thresh. (0.7 GeV/c)
Radius of 0.5 m and length of 2 m
16 modules, 60x2 scintillating tiles per module
15360 SiPMs (4 per scintillator side)
3840 channels

## Slide 26: The CBM TOF wall
Journal of Physics: Conf. Series 1023 (2018) 012007
M. Petris, ICHEP 2018
Compressed Barion Matter @ FAIR
• Au-Au interaction rate ~ 10 MHz
•Free ﬂowing DAQ with continuous R/O
Requirements:
  80 ps time resolution
  Rate up to 30 kHz/cm2
MRPC, double stack , 10 gaps of 140 mm
Low resistivity glass for Inner wall: 1010 Ω cm
Strip readout (0.254x4.6 cm2)
85% C2H2F4+ 5% i-C4H10+10% SF6
R/O: PADI chip + GET4 TDC

## Slide 27: Neural networks for MRPC time reconstruction
arXiv:1805.02833v1 [physics.ins-det] 8 May 2018
Typical signal processing by Time-over-Threshold
tp ~ particle arrival time
ttot~ signal amplitude for slewing correction
tp1
ttot1
tp2
ttot2
4-stage MRPC with 8 gaps of 104 mm and 0.5 mm plates +
Neural Network built using as input n equally spaced points along the leading edge →
tp : peak time
tl : length of leading edge
particle arrival time t0 = tp - tl
Real measurement using cosmics:
ToT s ~ 48 ps
NN s ~ 27 ps

## Slide 28: TPC for International Large Detector at ILC
Inner/Outer radius | 0.325/1.8 m
Length | 4.7 m
Gas | Ar/CF4/i-C4H10 (95/3/2)
Max n. of track samples | 222
B | 3.5 T
Point resolution srf | < 100 mm (1x6 mm2 R/O pads)
dE/dx resolution | 5%
dE/dx measurement | Truncated mean 70%
R/O chamber | GEM or MICROMEGAS + pad plane or Timepix
Nucl. Instr. and Meth. A 856 (2017) 109–118
EUDET/AIDA TPC prototype
3 GEM ROC, 70 mm hole, 140 mm pitch, 1.3x5.9 mm pad
Max drift length 57 cm, 28 track samples
77 cm
23 cm
17 cm
Testbeam results , B= 1 T
Extrapolation @ B= 3.5 T and Ldrift=2.35 m
Intrinsic s ~ 70 mm

## Slide 29: TPC for International Large Detector at ILC
Inner/Outer radius | 0.325/1.8 m
Length | 4.7 m
Gas | Ar/CF4/i-C4H10 (95/3/2)
Max n. of track samples | 222
B | 3.5 T
Point resolution srf | < 100 mm (1x6 mm2 R/O pads)
dE/dx resolution | 5%
dE/dx measurement | Truncated mean 70%
R/O chamber | GEM or MICROMEGAS + pad plane or Timepix
arXiv:1712.09777v1 [physics.ins-det] 28 Dec 2017
EUDET/AIDA TPC prototype
2 GEM ROC, 70 mm hole, 140 mm pitch, 1.3x5.9 mm pad + 1 gating GEM
Max drift length 57 cm, 28 track samples
Gating GEM with hexagonal holes, 25 mm thick
ILC beam structure
vdrift ~ 370 cm/s →
0.4 cm thick ion disc every 75 cm

## Slide 30: GEM-TPC with combined electronic and optical R/O
IEEE TNS, VOL. 65, NO. 3 (2018), 913-919
F. Brunbauer, 14th Pisa Meeting on advanced detectors 2018
Exploit CF4 scintillation for 3D track reconstruction → 2D imaging of projected track using a CCD camera + timing from electronic R/O of signals in transparent Indium Tin Oxide (ITO) strips anode
APV25 R/O time frame of 25 ns, e- drift velocity 8 cm/ms → z resolution ~ 2 mm
Arrival time of the signal on each anode strip determined by CFD with linear interpolation between data points
Proof of principle, large potentialities with different segmentation of ITO anode and faster R/O electronics to improve z resolution
(450 nm ITO film on glass, 48 x 1.5 mm strips by photolithography)
Hamamatsu ImagEM X2, 512x512 pixels of 16x16 mm2
Ar/CF4 (80/20)

## Slide 31: TR “imaging” using silicon sensors
E. Schioppa, 14th Pisa Meeting on advanced detectors 2018
Radiator
30 Mylar 50 mm,
3 mm gap
2.2 m He pipe
TimePix3
+
500 mm Si
beam
Extend PID to g>104 using energy and angular dependence of TR

## Slide 32: PICOSEC
arXiv:1806.04395v1 [physics.ins-det] 12 Jun 2018
F.J. Iguaz, 14th Pisa Meeting on advanced detectors 2018
80%Ne+10%C2H6+10%CF4
Radiator window: Cherenkov UV production.
Photocathode: UV -> electrons.
Two-stage Micromegas: drift (pre-amplification) + amplification gaps.
1st prototype tests, MgF2 radiator, CsI PC, single pad (1 cm diam.)
σ = 24 ps
Testbeam with 150 GeV m
New prototypes implementing:
resistive strips R/O to improve operation stability, up to 106 Hz/cm2
more robust PC (Al, CsI with protective layer, DLC)
multi-pads, 35 mm diam., 19 pads
σ = 36 ps
preliminary
Next R&D:
PC robustness and QE
Scalability and R/O electronics

## Slide 33: 3D Digital SiPM
Time-to-digital converter
PET Scanner
+
-
Start
Stop
Patient
Δ time = Δ distance
10 ps coincidence timing resolution (CTR) →
1.5 mm of precision, real time PET imaging
J.F. Pratte, 14th Pisa Meeting on advanced detectors2018
Conventional SiPM → array of SPADs (Single Photon Avalanche Diodes) connected in parallel
Main limitations for TOF-PET:
  SPAD to SPAD gain and dark count rate variations (response uniformity)
  Large output C affects rise-time
  timing skew associated to SPAD position
2D Digital SiPM:
  ↑ each SPAD connected to quenching circuit and TDC → low out C and time skew (individual calibration)
  ↓ Quite low fill factor
3D digital SiPM
High fill factor (up to 80%)
Heterogeneous technologies integration:
  SPAD array: Teledyne-Dalsa custom process
  TSMC CMOS 65 nm - 256 SPAD readout ASIC
first prototype
1.1x1.1 mm2 , 256 pixels
~ 500 ps time skew:
- clock and trigger distr.
- pixel to pixel variations
skew corrected
18 ps jitter
- R&D in progress
- Possible application in nEXO LAr experiment

## Slide 34: Conclusions
Experience with existing large systems has shown that the overall PID performance of state of art detectors can be improved as knowledge of detector response becomes more accurate and new signal processing and data analysis techniques can be applied (NN, combined PID, …).
The integration of micropattern gaseous detectors or hybrid solutions makes large TPCs an attractive solution for tracking and PID in future colliders (ILC, CEPC).
Also, MRPCs with improved rate capability (low resistivity glass) represent the best cost effective solution for large TOF systems (CBM).
“Fast timing” is (and will remain) the main R&D topic for upgrades and future applications. Solutions approaching the 10 ps regime are becoming available and implementation in real detectors is under development, although scaling to large systems is not straightforward.

## Slide 35
Backup slides

## Slide 36: PID basics
PID by interaction differentiation
measurement →
Cherenkov radiation: omitted
Specific ionization loss:
  N samples of thickness t along track → truncated mean (~0-80%) to cut Landau fluctuations
  , 5%-8% at P= 1 atm
  Primary collision cluster counting can provide better performance (with proper choice of gas, P, R/O pixel, FEE)
Time of flight:
  Separation power → fast detector, L
Transition radiation: e-/p separation
  (/ rad. sheet);
PID by mass measurement →
→ +

## Slide 37: PID basics
PID detectors dimensions
Particle Data Group, Phys. Rev. D 98, 030001 (2018)., Sect 34.6.6.
Nucl. Instr. & Meth. A 686 (2012), 148-172
Transition radiation
e-/p separation
p/K separation > 3s