## Slide 1: The missing movies in the last class.

## Slide 2: First particle detector using ionization: Leaf electroscope

## Slide 3: We want to observe any direct sign of particle passing by Eyes. Tiny effect stimulated by particle (Ionization) may sometime trigger a visible signature in matter
Supersaturated
Water solution of
sodium acetate
http://www.youtube.com/user/ikemonmon

## Slide 4: Cloud chamber animation

## Slide 5: Excitation and scintillation Aurora is a space plasma detector in the sky

## Slide 7: How can physicists explore the particle world? (II)
Junji Haba (KEK)
Moscow International School of Physics 2019

## Slide 8: The 2nd step
In the 1st step we review detection of particles through ionization, scintillation, Chrenkov radiation…etc.
Measuring/determining four momentum of particles is to combine the information from detector signals.
  Momentum, Energy, Velocity and more…

## Slide 10: Momentum
Momentum can be measured as a radius of circular motion in a magnetic field
B

## Slide 11: Lorentz force and momentum measurement
p
r
q or ze
s
sagitta

## Slide 12: What is necessary for better momentum measurement?

## Slide 13: Most popular tracking so far: Wire chambers invented by Charpak
Ionization

## Slide 14: Electron avalanche multiplication
Remember initial ionization is tiny signal

## Slide 15: The easiest way to provide high electric field
Electric field around a thin wire is extremly high
b
a
V

## Slide 16: Drift velocity

## Slide 17: Central Tracker

## Slide 18: Drift Chamber
Example of previous Belle CDC.
Curved Aluminum enplates for the main part.
  Thickness : 10mmt
Conical endplates for the inner part to give a space for accelerator components.
(momentum,PID)

## Slide 19: X-T relation (drift time vs position)
He(50%)-C2H6(50%)
B=1.5Tesla
HV : 2.3KV
Cell Size:18mm
Maximum Drift Time : ~400nsec
+
cell
+
+
+
+
+

## Slide 20
Inner part
5120 wires
Outer part
43,776 wires
Wire stringing for
BelleII central drift chamber
It took more than 5 years to complete

## Slide 21: Pt resolution of BelleII CDC
Before Align
After Align
Belle CDC only:
=> Estimate for Belle II :
Obtained : :
PT (GeV/c)
σrϕ: position resolution
B: magnetic field (1.5 T).
Χo: radiation length.
L: lever arm.
N: number of measurement point
Belle  Belle II
L: 77.5  94.84 cm
N: 50  56
PT resolution is much improved compare with Belle CDC.
Much better than the expectation (extrapolation from Belle CDC)
Observed constant term is not improved as expected because of the multiple scattering on the B-field mapper
Belle CDC
MC
No B-filed mapper
0.05p 0.7 (%)
~ CMS

## Slide 22: TPC(Time Projection Chamber)
Z-coordinate by drift time
Complete 3D measurement
CERN/ALICE Web page

## Slide 23: Straw Tubes Modules
Straw Tubes packed in double-layered modules
modules 64-cells wide
modules only ~0.37% of 1 X0
  “light” panels
  (Rohacell core with carbon fiber skins)
  “light” straws
x
z

## Slide 24: Scintillation strip/fiber tacker
0.5 – 1 mmf
0.25 mmf
Mu3e
T2K FGD

## Slide 25: Silicon tracker (LHC and HL-LHC)

## Slide 26: Energy measurement
Energy can be measured
by a total absorption calorimeter,
in which all the energy are released
through cascading shower.

## Slide 27: Energy measurement
Energy measurement with calorimetry is a powerful technique especially for higher energy experiment at hadron colliders.
  E ~ Number of particles generated in a shower (N)
  Cf.
Klaus Pretzl 2005 J. Phys. G: Nucl. Part. Phys. 31 R133
Traditional sampling calorimeter

## Slide 28: Particle identification
Particle identification (mass) can be made from its velocity（β=v/c）, which can be measured through time of flight, Cherenkov radiation or energy loss rate.
Life time (flight distance) of particle is another very important characteristics.
 | m ± | e ± | g | p ± | K0 | K ± | p | n
Mass (MeV/c2) | 106 | 0.511 | 0 | 140 | 498 | 494 | 938 | 940
Detection | Charge | Charge Shower | Shower | Charge Strong | Strong | Charge Strong | Charge Strong | Strong
Life time （ct m） | 659 | -- | -- | 7.8 | 0.027 (15.3) | 3.7 | -- | 2.7 x1011

## Slide 29: Velocity measurement

## Slide 30: Direct b measurement: ToF (Time of Flight)

## Slide 31: b measurement through energy loss information
Remember Bethe-Bloch formulation
Effective aet low enrgy

## Slide 32: ToF and dE/dx to distinguish p/K/p

## Slide 33: Velocity from Cherenkov radiation

## Slide 34: Photomultiplier
Vacuum tube surviving even now
Important notion
Photoelectric effect
Quantum efficeincy
Poisson statistics
Seconary electron
Vulnerable to magnetic field
HPK PMT Handbook
Photon
Phocathode
Dynode
Anode
High sensitivity
photon sensor Needed!

## Slide 35
The first documented photomultiplier demonstration dates to the early 1934 accomplishments of an RCA group based in Harrison, NJ. Harley Iams and Bernard Salzberg were the first to integrate a photoelectric-effect cathode and single secondary emission amplification stage in a single vacuum （Wikipedia)
PD15@INR

## Slide 36: Hybrid detector
Photocathode
Multi-pixel AD
Proximity focus
(8kV)
AD voltage
(-200 to -400 V)
EB gain (x1200)
Acceleration
Avalanche gain (x40)
Photon
Electron
Output
Total gain:
5x104
HPD with Multi-pixel Avalanche Diode (AD-HPD)

## Slide 37: Timing Resolution for small HPD
 | Resolution (σ)
f8 mm | 21 ps
f1 mm | 14 ps
including jitter of electronics
Notes: This figure shows timing resolution of HPD for full illumination on photocathode. The result was 41 ps.
On the other hand, in other measurement system, PLP waveform was measured by a streak-camera having extremely high timing resolution to discuss the limiting factor. The pulse width of PLP was 30 ps in sigma.
There was big difference between PLP pulse width and the result of HPD.
So, we measured the timing resolution for spot illumination on photocathode to investigate the limiting factor.
The result was 31 ps in sigma for the spot illumination of 1 mm in diameter.
As you can see it, It is almost consistent with the PLP waveform.

## Slide 38: HAPD Belle II
~5mm pixel size. Large coverage.
Immune to 1.5T magnetic field.
Radiation tolerance (neutron, gamma).
Photo-detector
HAPD (Hybrid Avalanche Photo-Detector)
Developed with Hamamatsu Photonics.
144 channels (36-ch APD chip×4).
Gain ≥45000.
Peak QE ~28%
Size 73mm×73mm.
Effective area 63mm×63mm (65%).
Total 420 HAPDs

## Slide 39: Belle II A-RICH

## Slide 42
PD18 Matsuoka

## Slide 43
Bialkali: SbKCs, SbRbCs Multialkali: SbNa2KCs (alkali metals have low work function)
QE’s of typical photo-cathodes
from T. Gys, Academic Training, 2005

## Slide 44: Lesson from HK PMT development

## Slide 45: Solid state photosensors: Photodiode
Inner Photoelectric effect, high QE.
Immune to magnetic field
Very compact in general
Sensitivity not close to 1pe

## Slide 46: Avalanche Photodiode, APD (CMS version)
Photo-conversion electrons from the thin p-layer(deff ~ 6 m) induce avalanche amplification at the p-n junction.
Impact ionization
Electrons created by ionising particles traversing the bulk are not amplified.

## Slide 47: Geiger mode APD multipixel array
Originally invented and developed by Russian researchers, Solid State Photodetectors group led by Dr. V. Shubin, Dr. Z. Sadygov and his colleagues at the INR/MELZ collaboration, the MEPhI/Pulsar collaboration led by Prof. B. Dolgoshein.
Since mid-2000s many companies in the world have started development and improved the technology with various names like ,
  SiPM
  MRS-APD
  SPM
  MPGM APD
  AMPD
  GM-APD
  MPPC

## Slide 48: Principle of operation
Musienko @PD07
-Vbias
output


APD
Remember avalanche process for tiny signal

## Slide 49: Afterpulsing
Some portion of carriers generated in an avalanche would be trapped in lattice defects and then released with triggering another avalanche.
NC = No. of carriers = Gain
Pt = Trap probability
t = Trap lifetime
Pav = Geiger discharge
probability
Low gain, low Pt, or long t gives
low Pap

## Slide 50: Reducing after pulses
Thinner epi layer (compromise long l sensitivity though) contributing to signal
Less defects. Epi quality or gettering technology.

## Slide 51: Less crosstalks
Separation trenches can help to reduce crosstalk rate.
Yamamoto@PD07

## Slide 53: Recent improvements are dramatic

## Slide 54: Photon detection with Gas multiplication
Not yet widely used as standard technique.
IFB is an issue.
  PHOTON DETECTOR
  MWPC with CH4 at
  atmospheric pressure
  (4 mm sensitive gap)
  analogue pad readout
  (~160 103 channels)
  reflective layer of CsI
  (QE  25% @ 175 nm)
ALICE HMPID

## Slide 55: CsI+ 2THGEM+MICROMEGAS
COMPASS RICH-1 upgrade
To expect less IFB

## Slide 56: CERN NA62

## Slide 57: CEDAR Gas Cherenkov
0.55 f x 4.5 m
45MHz 100psec resolution required

## Slide 58: NA62 RICH

## Slide 59: NA62 MUV